## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #15
Simplification

## Slide 2: Slido Link
You can ask questions here:
https://app.sli.do/event/4fVqZQwmoM7yUV24bQvuhp
Or scan this QR code. May be obstructed in some slides.

## Slide 3: Lecture #15: Simplification
Function Simplification
Algebraic Simplification
Half Adder
Gray Code
K-maps
  5.1 Introduction
  5.2 How to use K-maps
  5.3 Converting to Minterms Form
  5.4 Prime Implicants (PIs) and Essential Prime Implicants (EPIs)
  5.5 Finding Simplified SOP Expression
  5.6 Finding Simplified POS Expression
  5.7 Don’t-care Conditions
More Examples

## Slide 4: 1. Function Simplification
Why simplify?
  Simpler expression leads to circuit that uses fewer logic gates.
  Thus cheaper, uses less power, (sometimes) faster.
Techniques
  Algebraic
    Using theorems
    Open-ended; requires skills
  Karnaugh Maps
    Easy to use
    Limited to no more than 6 variables
  Quine-McCluskey (non-examinable)
    Suitable for automation
    Can handle many variables (but computationally intensive)

## Slide 5: 2. Algebraic Simplification (1/3)
Aims to minimise
  Number of literals, and
  Number of terms
But sometimes conflicting, so let’s aim at reducing the number of literals for the examples in the next few slides.
Challenging – requires good algebraic manipulation skills.

## Slide 6: 2. Algebraic Simplification (2/3)
Example 1: Simplify (x+y)(x+y')(x'+z)
  (x+y)(x+y')(x'+z) = (xx + xy' + xy + yy')  (x'+z) (distributivity) = (x + xy' + xy + yy')  (x'+z) (idempotency) = (x + x(y'+y) + yy')  (x'+z) (distributivity) = (x + x(1) + 0)  (x'+z) (complement) = (x + x)  (x'+z) (identity) = x  (x'+z) (idempotency) = xx' + xz (distributivity) = 0 + xz (complement) = xz (identity)
Number of literals reduced from 6 to 2.

## Slide 7: 2. Algebraic Simplification (3/3)
Example 2: Find the simplified SOP expression of F(a,b,c,d) = abc + abd + a'bc' + cd + bd'
  abc + abd + a'bc' + cd + bd' = abc + ab + a'bc' + cd + bd' (absorption 2) = abc + ab + bc' + cd + bd' (absorption 2) = ab + bc' + cd + bd' (absorption 1) = ab + cd + b(c'+d') (distributivity) = ab + cd + b(cd)' (DeMorgan’s) = ab + cd + b (absorption 2) = b + cd (absorption 1)
Number of literals reduced from 13 to 3.
abd + bd'
= b (ad + d')
= b (a + d')
= ab + bd'


## Slide 8: 3. Half Adder (1/2)
Half adder is a circuit that adds 2 single bits (X, Y) to produce a result of 2 bits (C, S).
The black-box representation and truth table for half adder are shown below.
Inputs |  | Outputs | 
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Half adder
X
Y
(X+Y)
S
C


## Slide 9: 3. Half Adder (2/2)
In canonical form (sum-of-minterms):
  C = X∙Y
  S = X'∙Y + X∙Y'
Output S can be simplified further (though no longer in SOP form):
  S = X'∙Y + X∙Y' = X  Y
Implementation of a half adder
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C

## Slide 10: 4. Gray Code (1/3)
Unweighted (not an arithmetic code)
Only a single bit change from one code value to the next.
Not restricted to decimal digits: n bits  2n values.
Good for error detection.
Named after Frank Gray; also called reflected binary code.
Example: 4-bit standard Gray code

## Slide 11: 4. Gray Code (2/3)
There are many Gray code sequences.
Example: For 3 bits, here are some possible Gray code sequences:
000
001
011
010
110
111
101
100
000
010
110
111
011
001
101
100
110
111
101
100
000
001
011
010
000
001
010
011
100
101
110
111
010
110
101
001
100
111
000
011
010
011
111
110
111
101
001
000



This is the standard Gray Code.
These are NOT Gray codes (why?)

## Slide 12: 4. Gray Code (3/3)
Generating a 4-bit standard Gray code sequence.
0 0 0 0
0 0 0 1
0 0 0 1
0 0 0 0
0 0 1 0
0 0 1 1
0 0 0 1
0 0 0 0
0 1 0 0
0 1 0 1
0 1 1 1
0 1 1 0
0 0 1 0
0 0 1 1
0 0 0 1
0 0 0 0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
How to generate 5-bit standard Gray code sequence? 6-bit standard Gray code sequence?
You may refer to Digital Logic Design (Chapter 2, Section 2.12 Gray Code) on the algorithms to convert binary to Gray code and vice versa.

## Slide 13: 5.1 Introduction to K-maps
Systematic method to obtain simplified sum-of-products (SOP) expressions.
Objective: Fewest possible product terms and literals.
Diagrammatic technique based on a special form of Venn diagram.
Advantage: Easy to use.
Disadvantage: Limited to 5 or 6 variables.
Karnaugh-map (K-map) is an abstract form of Venn diagram, organised as a matrix of squares, where
  Each square represents a minterm
  Two adjacent squares represent minterms that differ by exactly one literal

## Slide 14: 5.1 2-Variable K-maps (1/3)
Let the 2 variables be a and b. The K-map can be drawn as…
Alternative layouts of a 2-variable (a, b) K-map:
a'∙b'
a∙b'
a'∙b
a∙b
b
a
m0
m2
m1
m3
b
a
OR
Alternative 2:
a'∙b'
a'∙b
a∙b'
a∙b
a
b
m0
m1
m2
m3
a
b
Alternative 1:
OR
a∙b
a'∙b
a∙b'
a'∙b'
b
a
m3
m1
m2
m0
b
a
OR
Alternative 3:
and others…

## Slide 15: 5.1 2-Variable K-maps (2/3)
Alternative labelling of a 2-variable (a, b) K-map:
a
b
equivalent to:
a
b
0 1
0
1
b
a
equivalent to:
b
a
1 0
0
1

## Slide 16: 5.1 2-Variable K-maps (3/3)
The K-map for a function is filled by putting
  A ‘1’ in the square the corresponds to a minterm of the function
  A ‘0’ otherwise
Example: Half adder.
0
0
0
0
0
a
b
a
b
C = a∙b
S = a∙b' + a'∙b
1
1
1


## Slide 17: 5.1 3-Variable K-maps (1/2)
As there are 8 minterms for 3 variables, so there are 8 squares in a 3-variable K-map.
Example: Let the variables be a, b, c.
a∙b'∙c'
a∙b'∙c
a
b
a∙b∙c
a∙b∙c'
a'∙b'∙c'
a'∙b'∙c
a'∙b∙c
a'∙b∙c'
0
1
00 01 11 10
c
a
bc
OR
m4
m5
a
b
m7
m6
m0
m1
m3
m2
c
a
bc
0
1
00 01 11 10
Note Gray code sequence
A Gray code sequence is one where the value differs from its previous by 1 bit.
Above arrangement ensures that minterms of adjacent cells differ by only ONE literal. (Other arrangements which satisfy this criterion may also be used.)

## Slide 18: 5.1 3-Variable K-maps (2/2)
There is wrap-around in the K-map:
  a'∙b'∙c' (m0) is adjacent to a'∙b∙c' (m2)
  a∙b'∙c' (m4) is adjacent to a∙b∙c' (m6)
m4
m5
m7
m6
m0
m1
m3
m2
0
1
00 01 11 10
a
bc
Each cell in a 3-variable K-map has 3 adjacent neighbours. For example, m0 has 3 adjacent neighbours: m1, m2 and m4.
In general, each cell in an n-variable K-map has n adjacent neighbours.

## Slide 19: Quick Review Questions #1
DLD page 106, questions 5-1 to 5-2.
5-1. The K-map of a 3-variable function F is shown below. What is the sum-of-minterms expression of F?
5-2. Draw the K-map for this function A:
A(x, y, z) = x∙y + y∙z' + x'∙y'∙z
0
1
a
b
0
0
1
0
0
1
0
1
00 01 11 10
c
a
bc
m(0, 2, 5)
= a'∙b'∙c' + a'∙b∙c' + a∙b'∙c
x
y
z
1
1
1
1
0
0
0
0


## Slide 20: 5.1 4-Variable K-maps (1/2)
There are 16 square cells in a 4-variable K-map.
Example: Let the variables be w, x, y, z.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 21: 5.1 4-Variable K-maps (2/2)
There are 2 wrap-arounds.
Every cell has 4 neighbours.
  Example: The cell corresponding to minterm m0 has neighbours m1, m2, m4 and m8.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 22: 5.1 5-Variable K-maps (1/2)
K-maps of more than 4 variables are more difficult to use because the geometry (hypercube configurations) for combining adjacent squares becomes more involved.
For 5 variables, e.g. v, w, x, y, z, we need 25 = 32 squares.
Each square has 5 neighbours.

## Slide 23: 5.1 5-Variable K-maps (2/2)
Organised as two 4-variable K-maps. One for v' and the other for v.
m20
m21
w
y
m23
m22
m16
m17
m19
m18
00
01
11
10
00 01 11 10
z
wx
yz
m28
m29
m31
m30
m24
m25
m27
m26
x
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x
v '
v
Corresponding squares of each map are adjacent.
Can visualise this as one 4-variable K-map being on TOP of the other 4-variable K-map.

## Slide 24: 5.1 Larger K-maps (1/2)
6-variable K-map is pushing the limit of human’s “pattern-recognition” capability.
K-maps larger than 6 variables are practically unheard of!
Normally, a 6-variable K-map is organised as four 4-variable K-maps, mirrored along two axes.

## Slide 25: 5.1 Larger K-maps (2/2)
a'∙b'
m0
00 01
11
10
00 01 11 10
cd
ef
m1
m3
m2
m4
m5
m7
m6
m12
m13
m15
m14
m8
m9
m11
m10
m40
10 11
01
00
00 01 11 10
cd
ef
m41
m43
m42
m44
m45
m47
m46
m36
m37
m39
m38
m32
m33
m35
m34
m18
00 01
11
10
10 11 01 00
cd
ef
m19
m17
m16
m22
m23
m21
m20
m30
m31
m29
m28
m26
m27
m25
m24
m58
10 11
01
00
10 11 01 00
cd
ef
m59
m57
m56
m62
m63
m61
m60
m54
m55
m53
m52
m50
m51
m49
m48
a'∙b
a∙b'
a∙b
a
b
Try stretching your recognition capability by finding simplest sum-of-products expression for S m(6,8,14,18,23,25,27,29,41,45,57,61).

## Slide 26: 5.2 How to Use K-maps (1/7)
Based on the Unifying Theorem (complement law):
  A + A' = 1
In a K-map, each cell containing a ‘1’ corresponds to a minterm of a given function F where the output is 1.
Each valid grouping of adjacent cells containing ‘1’ then corresponds to a simpler product term of F.
  A group must have size in powers of two: 1, 2, 4, 8, …
  Grouping 2 adjacent cells eliminates 1 variable from the product term; grouping 4 cells eliminates 2 variables; grouping 8 cells eliminates 3 variables, and so on. In general, grouping 2n cells eliminates n variables.

## Slide 27: 5.2 How to Use K-maps (2/7)
Group as many cells as possible
  The larger the group, the fewer the number of literals in the resulting product term.
Select as few groups as possible to cover all the cells (minterms) of the function
  The fewer the groups, the fewer is the number of product terms in the simplified SOP expression.

## Slide 28: 5.2 How to Use K-maps (3/7)
Example:
F (w,x,y,z) = w'∙x∙y'∙z' + w'∙x∙y'∙z + w∙x'∙y∙z'
+ w∙x'∙y∙z + w∙x∙y∙z' + w∙x∙y∙z
=  m(4, 5, 10, 11, 14, 15)
1
1
1
1
1
1
w
y
00
01
11
10
00 01 11 10
wx
yz
x
z
0
0
0
0
0
0
0
0
0
0

## Slide 29: 5.2 How to Use K-maps (4/7)
Each group of adjacent minterms corresponds to a possible product term of the given function.
Here, there are 2 groups of minterms, A and B:
  A = w'.x.y'.z' + w'.x.y'.z = w'.x.y'.(z' + z) = w'.x.y'
  B = w.x'.y.z' + w.x'.y.z + w.x.y.z' + w.x.y.z
  = w.x'.y.(z' + z) + w.x.y.(z' + z)
  = w.x'.y + w.x.y
  = w.(x'+x).y
  = w.y
A
B
1
1
1
1
1
1
w
00
01
11
10
00 01 11 10
z
wx
yz
x
y
0
0
0
0
0
0
0
0
0
0

## Slide 30: 5.2 How to Use K-maps (5/7)
Each product term that corresponds to a group, w'∙x∙y' and w∙y, represents the sum of minterms in that group.
Boolean expression is therefore the sum of product terms (SOP) that represent all groups of the minterms of the function:
  F(w,x,y,z) = group A + group B = w'∙x∙y' + w∙y

## Slide 31: 5.2 How to Use K-maps (6/7)
The larger the group (the more minterms it contains), the fewer is the number of literals in the associated product term.
  Recall that a group must have size in powers of two.
  Example: For a 4-variable K-map with variables w, x, y, z 1 cell = 4 literals. Examples: w∙x∙y∙z, w'∙x∙y'∙z 2 cells = 3 literals. Examples: w∙x∙y, w∙y'∙z' 4 cells = 2 literals. Examples: w∙x, x'∙y 8 cells = 1 literal. Examples: w, y', z 16 cells = no literal (i.e. logical constant 1). Example: 1

## Slide 32: 5.2 How to Use K-maps (7/7)
Examples of valid and invalid groupings.
1
1
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
P
P
1
1
1
1
1
1
1
1
1
1
1
1
1
1
O
1
1
1
1
1
1
O

## Slide 33: 5.3 Converting to Minterms Form (1/2)
The K-map of a function can be easily filled in when the function is given in sum-of-minterms form.
What if it is not in sum-of-minterms form?
  Convert it into sum-of-products (SOP) form
  Expand the SOP expression into sum-of-minterms expression, or fill in the K-map directly based on the SOP expression.

## Slide 34: 5.3 Converting to Minterms Form (2/2)
Example:
  F(A,B,C,D) = A.(C+D)'.(B'+D') + C.(B+C'+A'.D) = A.(C'.D').(B'+D') + B.C + C.C' + A'.C.D = A.B'.C'.D' + A.C'.D' + B.C + A'.C.D
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
A.B'.C'.D' + A.C'.D' + B.C + A'.C.D
= A.B'.C'.D' + A.C'.D'.(B+B') + B.C + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B'.C'.D' + B.C.(A+A') + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B.C + A'.B.C + A'.C.D
= A.B'.C'.D' + A.B.C'.D' + A.B.C.(D+D') + A'.B.C.(D+D') + A'.C.D.(B+B')
= A.B'.C'.D' + A.B.C'.D' + A.B.C.D + A.B.C.D' + A'.B.C.D + A'.B.C.D' + A'.B'.C.D
Expanding it to sum of minterms (unnecessary):
0
0
0
0
0
0
0
0
0

## Slide 35: 5.4 PIs and EPIs (1/3)
To find the simplest (minimal) SOP expression from a K-map, you need to obtain:
  Minimum number of literals per product term; and
  Minimum number of product terms.
Achieved through K-map using
  Bigger groupings of minterms (prime implicants) where possible; and
  No redundant groupings (look for essential prime implicants)
Implicant: a product term that could be used to cover minterms of the function.

## Slide 36: 5.4 PIs and EPIs (2/3)
Prime implicant (PI): a product term obtained by combining the maximum possible number of minterms from adjacent squares in the map. (That is, it is the biggest grouping possible.)
Always look for prime implicants in a K-map.
1
1
1
1
1
1
O
1
1
1
1
1
1
P

## Slide 37: 5.4 PIs and EPIs (3/3)
No redundant groups:
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
O
1
1
Essential prime implicant (EPI): a prime implicant that includes at least one minterm that is not covered by any other prime implicant.
Essential prime implicants

## Slide 38: Quick Review Questions #2

DLD page 106, question 5-3.
5-3. Identify the prime implicants and essential prime implicants of the two K-maps below.
0
1
a
b
0
0
1
1
0
1
0
1
00 01 11 10
c
a
bc
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
1
1
1
1
How many PIs?
3 PIs
How many EPIs?
2 EPIs
How many PIs?
7 PIs
How many EPIs?
4 EPIs
0
0
0
0
0

## Slide 39: 5.5 Finding Simplified SOP Expression (1/4)
Algorithm
    Circle all prime implicants on the K-map.
    Identify and select all essential prime implicants for the cover.
    Select a minimum subset of the remaining prime implicants to complete the cover, that is, to cover those minterms not covered by the essential prime implicants.

## Slide 40: 5.5 Finding Simplified SOP Expression (2/4)
1
1
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
D
1
1
Example #1:
F(A,B,C,D) = S m(2,3,4,5,7,8,10,13,15)
All prime implicants
0
0
0
0
0
0
0


## Slide 41: 5.5 Finding Simplified SOP Expression (3/4)
B
1
1
C
A
00
01
11
10
00 01 11 10
CD
AB
1
1
1
1
D
1
1
1
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
Essential prime implicants
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
Answer
All PIs


## Slide 42: 5.5 Finding Simplified SOP Expression (4/4)
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
B∙D
A∙B'∙D'
A'∙B∙C'
A'∙B'∙C
F(A,B,C,D) = B∙D + A'∙B∙C' + A∙B'∙D' + A'∙B'∙C

0
0
0
0
0
0
0

## Slide 43: Quick Review Questions #3

DLD pages 106-107, questions 5-4 to 5-7.
5-4. Find the minimal SOP expression for G(A,B,C,D).
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
1
1
Prime implicants?
Essential prime implicants?
0
0
0
0
0
0
0
0
B∙D,
A'∙B∙C',
A∙C'∙D,
A∙B∙C,
A'∙C∙D
All, except B∙D, are essential.
G = A'∙B∙C' + A∙C'∙D + A∙B∙C + A'∙C∙D

## Slide 44: 5.6 Finding Simplified POS Expression (1/2)
Simplified POS expression can be obtained by grouping the maxterms (i.e. 0s) of the given function.
Example:
  Given F = Sm(0,1,2,3,5,7,8,9,10,11), we first draw the K-map, then group the maxterms together:
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
0
1
1
D
1
1
1
1
1
0
0
0
0
0

## Slide 45: 5.6 Finding Simplified POS Expression (2/2)
This gives the SOP of F' to be F' = BD' + AB
To get POS of F, we have
  F = (BD' + AB)' = (BD')'  (AB)' (DeMorgan) = (B'+D)  (A'+B') (DeMorgan)
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
0
1
1
D
1
1
1
1
1
0
0
0
0
0
K-map of F
0
0
C
A
00
01
11
10
00 01 11 10
B
CD
AB
0
1
0
0
D
0
0
0
0
0
1
1
1
1
1
K-map of F'


## Slide 46: 5.7 Don’t-Care Conditions (1/5)
In certain problems, some outputs are not specified or are invalid. Hence, these outputs can be either ‘1’ or ‘0’.
They are called don’t-care conditions, denoted by X (or d).
Example: A circuit takes in a 3-bit value ABC and outputs 2-bit value FG which is the sum of the input bits. It is also known that inputs 000 and 111 never occur.
A | B | C | F | G
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Assuming all inputs are valid.
A | B | C | F | G
0 | 0 | 0 | X | X
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | X | X
Assuming inputs 000 and 111 are invalid.

## Slide 47: 5.7 Don’t-Care Conditions (2/5)
Don’t-care conditions can be used to help simplify Boolean expression further in K-maps.
They could be chosen to be either ‘1’ or ‘0’, depending on which choice results in a simpler expression.
We usually use the notation Sd to denote the set of don’t-care minterms.
A | B | C | F | G
0 | 0 | 0 | X | X
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | X | X
Assuming inputs 000 and 111 are invalid.
  Example:
  F(A,B,C) = Sm(3, 5, 6) + Sd(0, 7)
  G(A,B,C) = Sm(1, 2, 4) + Sd(0, 7)

## Slide 48: 5.7 Don’t-Care Conditions (3/5)
Comparison
  With don’t-cares:
  Without don’t-cares:
  F(A,B,C) = Sm(3, 5, 6, 7)
  G(A,B,C) = Sm(1, 2, 4, 7)
  F(A,B,C) = Sm(3, 5, 6) + Sd(0, 7)
  G (A,B,C)= Sm(1, 2, 4) + Sd(0, 7)
A
B
C
0
0
G
1
1
1
1
0
0
  F = A∙C + A∙B + B∙C
  G = A∙B'∙C' + A'∙B'∙C + A∙B∙C + A'∙B∙C'
A
B
C
1
0
F
0
0
0
1
1
1
  F = A∙C + A∙B + B∙C
A
B
C
1
X
F
0
0
0
X
1
1
A
B
C
0
X
G
1
1
1
X
0
0
  G = B'∙C' + A'∙B' + A'∙C'

## Slide 49: 5.7 Don’t-Care Conditions (4/5)
Suppose you are given the truth table for a function F(K,L,M,N) as follows:
?
K
L
M
N
F

X
Y
S
C

X
Y
S
C
K | L | M | N | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
You are also told that the inputs K, L, M, N are taken from the outputs of two half adders as shown:
Then you may revise the truth table:
X
X
X
X
X
X
X

## Slide 50: 5.7 Don’t-Care Conditions (5/5)
K-map of F:
K | L | M | N | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | X
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | X
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X
X
0
K
M
00
01
11
10
00 01 11 10
N
X
X
0
0
L
1
1
0
1
X
X
X
0
0
X
PIs: K'∙M, L∙M, and K∙M'∙N'
(Note: K∙L and M∙N not considered PIs as they consist of only X’s.)
EPIs: K'∙M and K∙M'∙N'
Simplified SOP:
F = K'∙M + K∙M'∙N'

## Slide 51: 6. More Examples (1/6)
Example #2:
F(A,B,C,D) = ABC + B'CD' + AD + B'C'D'
Fill in the 1’s and 0’s.
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
D
1
1
1
1
0
0
0
0
0
0
0

## Slide 52: 6. More Examples (2/6)
Example #2:
F(A,B,C,D) = ABC + B'CD' + AD + B'C'D'
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
D
1
1
1
1
0
0
0
0
0
0
0
Find all PIs:
AD
AC
AB'
B'D'
A.D, A.C and B'.D' are EPIs, and they cover all the minterms.
So the answer is: F(A,B,C,D) = AD + AC + B'D'


## Slide 53: 6. More Examples (3/6)
Example #3 (with don’t-cares):
F(A,B,C,D) = Sm(2,8,10,15) + Sd(0,1,3,7)
Fill in the 1’s and X’s.
1
X
C
A
00
01
11
10
00 01 11 10
B
CD
AB
X
1
X
D
1
1
X
0
0
0
0
0
0
0
0

## Slide 54: 6. More Examples (4/6)
Example #3 (with don’t-cares):
F(A,B,C,D) = Sm(2,8,10,15) + Sd(0,1,3,7)
1
X
C
A
00
01
11
10
00 01 11 10
B
CD
AB
X
1
X
D
1
1
X
0
0
0
0
0
0
0
0
Do we need to have an additional term A'B' to cover the 2 remaining X’s?
No, because all the 1’s (minterms) have been covered.
Answer: F(A,B,C,D) = B'D' + BCD


## Slide 55: 6. More Examples (5/6)

Find the simplest POS expression for example #2: F(A,B,C,D) = ABC + B'CD' + AD + B'C'D'
Draw the K-map of the complement of F, that is, F'.
From K-map,
F' = A'B + A'D + BC'D'
Using DeMorgan’s theorem,
F = (A'B + A'D + BC'D')'
= (A+B')(A+D')(B'+C+D)
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
D
1
1
1
0
0
0
0
0
0
0
0
0
K-map of F'

## Slide 56: 6. More Examples (6/6)

Find the simplest POS expression for example #3: F(A,B,C,D) = Sm(2,8,10,15) + Sd(0,1,3,7)
Draw the K-map of the complement of F, that is, F'. F'(A,B,C,D) = Sm(4,5,6,9,11,12,13,14) + Sd(0,1,3,7)
From K-map,
F ' = BC' + BD' + B'D
Using DeMorgan’s theorem,
F = (BC' + BD' + B'D)'
= (B'+C)(B'+D)(B+D')
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
D
1
1
1
X
X
X
X
1
0
0
0
0
K-map of F'

## Slide 57: Reading
Alternative Solutions
  Read up DLD section 5.8, pg 101.
Quine-McCluskey
  Not included in syllabus, but helps in further understanding.
  Read up DLD section 5.10, pg 103 – 105.

## Slide 58: End of File