## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #20
Pipelining
Part I: Introduction

## Slide 2: Lecture #20: Pipelining I
Introduction
MIPS Pipeline Stages
Pipeline Datapath
Pipeline Control
Pipeline Performance

## Slide 3: 1. Introduction: Inspiration
Assembly Line

## Slide 4: 1. Introduction: Inspiration

## Slide 5: 1. Introduction: Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold and stash
Washer takes 30 minutes
Dryer takes 30 minutes
“Folder” takes 30 minutes
“Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 6: 1. Introduction: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
Steady state: 1 load every 2 hours
If they learned pipelining, how long would laundry take?
30
T
a
s
k
O
r
d
e
r
B
C
D
A
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 7: 1. Introduction: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
Steady state: 1 load every 30 minutes
Potential speedup = 2 hr/30 min = 4 (no. of stages)
Time to fill pipeline takes 2 hours  speedup 
T
a
s
k
O
r
d
e
r
B
C
D
A
Time
6 PM
7
8
9
10
11
12
1
2 AM
30
30
30
30
30
30
30

## Slide 8: 1. Introduction: What If: Slow Dryer
Pipelined laundry now takes 5.5 hours!
Steady state: One load every 1 hour (dryer speed)
Pipeline rate is limited by the slowest stage
T
a
s
k
O
r
d
e
r
B
C
D
A
Time
6 PM
7
8
9
10
11
12
1
2 AM
30
30
30
30
30
30
30
30
30
30
30

## Slide 9: 1. Introduction: What If: Dependency
Brian is using the laundry for the first time; he wants to see the outcome of one wash + dry cycle first before putting in his clothes
Pipelined laundry now takes 4 hours
T
a
s
k
O
r
d
e
r
B
C
D
A
Time
6 PM
7
8
9
10
11
12
1
2 AM
30
30
30
30
30
30
30
30
Dependency
Stall

## Slide 10: 1. Introduction: Pipelining Lessons
Pipelining doesn’t help latency of single task:
  It helps the throughput of entire workload
Multiple tasks operating simultaneously using different resources
Possible delays:
  Pipeline rate limited by slowest pipeline stage
  Stall for dependencies

## Slide 11: 2. MIPS Pipeline Stages (1/2)
Five Execution Stages
  IF: Instruction Fetch
  ID: Instruction Decode and Register Read
  EX: Execute an operation or calculate an address
  MEM: Access an operand in data memory
  WB: Write back the result into a register
Idea:
  Each execution stage takes 1 clock cycle
  General flow of data is from one stage to the next
Exceptions:
  Update of PC and write back of register file – more about this later…

## Slide 12: 2. MIPS Pipeline Stages (2/2)

## Slide 13: 2. Pipelined Execution: Illustration
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Program Flow
(Instructions)
Time
Several instructions are in the pipeline simultaneously!

## Slide 14: 3. MIPS Pipeline: Datapath (1/3)
Single-cycle implementation:
  Update all state elements (PC, register file, data memory) at the end of a clock cycle
Pipelined implementation:
  One cycle per pipeline stage
  Data required for each stage needs to be stored separately (why?)

## Slide 15: 3. MIPS Pipeline: Datapath (2/3)
Data used by subsequent instructions:
  Store in programmer-visible state elements: PC, register file and memory
Data used by same instruction in later pipeline stages:
  Additional registers in datapath called pipeline registers
  IF/ID: register between IF and ID
  ID/EX: register between ID and EX
  EX/MEM: register between EX and MEM
  MEM/WB: register between MEM and WB
Why no register at the end of WB stage?

## Slide 16: 3. MIPS Pipeline: Datapath (3/3)
Coloured rectangles are pipeline registers

## Slide 17: 3. Pipeline Datapath: IF Stage
At the end of a cycle, IF/ID receives (stores):
  Instruction read from InstructionMemory[ PC ]
  PC + 4
PC + 4
  Also connected to one of the MUX's inputs (another coming later)

## Slide 18: 3. Pipeline Datapath: ID Stage
At the beginning of a cycle IF/ID register supplies: | At the end of a cycle ID/EX receives:
Register numbers for reading two registers 16-bit offset to be sign-extended to 32-bit PC + 4 | Data values read from register file 32-bit immediate value PC + 4

## Slide 19: 3. Pipeline Datapath: EX Stage
At the beginning of a cycle ID/EX register supplies: | At the end of a cycle EX/MEM receives:
Data values read from register file 32-bit immediate value PC + 4 | (PC + 4) + (Immediate x 4) ALU result isZero? signal Data Read 2 from register file

## Slide 20: 3. Pipeline Datapath: MEM Stage
At the beginning of a cycle EX/MEM register supplies: | At the end of a cycle MEM/WB receives:
(PC + 4) + (Immediate x 4) ALU result isZero? signal Data Read 2 from register file | ALU result Memory read data

## Slide 21: 3. Pipeline Datapath: WB Stage
At the beginning of a cycle MEM/WB register supplies: | At the end of a cycle
ALU result Memory read data | Result is written back to register file (if applicable) There is a bug here…….

## Slide 22: 3. Corrected Datapath (1/2)
Observe the “Write register” number
  Supplied by the IF/ID pipeline register
  It is NOT the correct write register for the instruction now in WB stage!
Solution:
  Pass “Write register” number from ID/EX through EX/MEM to MEM/WB pipeline register for use in WB stage
  i.e. let the "Write register" number follows the instruction through the pipeline until it is needed in WB stage

## Slide 23: 3. Corrected Datapath (2/2)

## Slide 24: 4. Pipeline Control: Main Idea
Same control signals as single-cycle datapath
Difference: Each control signal belongs to a particular pipeline stage

## Slide 25: 4. Pipeline Control: Try it!
Try associating each control signal with the correct pipeline stage.

## Slide 26: 4. Pipeline Control: Grouping
Group control signals according to pipeline stage
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1
 | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDst | ALUSrc | ALUop |  | Mem Read | Mem Write | Branch | MemToReg | Reg Write
 |  |  | op1 | op0 |  |  |  |  | 
R-type | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
lw | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
sw | X | 1 | 0 | 0 | 0 | 1 | 0 | X | 0
beq | X | 0 | 0 | 1 | 0 | 0 | 1 | X | 0

## Slide 27: 4. Pipeline Control: Implementation
Signal generated in ID stage
Signal used in EX stage and onwards
Signal propagated along until utilized

## Slide 28: 4. Pipeline Control: Datapath and Control

## Slide 29: 5. Different Implementations
Multi-Cycle
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
Load
Store
IF
R-type
Pipeline
Load
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
Clk
Cycle 1
Cycle 2
Load
Store
Waste
Single-Cycle

## Slide 30: 5. Comparison of Performance (1/2)
Cycle time:
  = Time for operation in stage k
  N = Number of stages
Execution Time for I instructions:
  =
Single-Cycle Processor
Instruction | Inst Mem | Reg read | ALU | Data Mem | Reg write | Total
ALU (eg: add) | 2 | 1 | 2 |  | 1 | 6
lw | 2 | 1 | 2 | 2 | 1 | 8
sw | 2 | 1 | 2 | 2 |  | 7
beq | 2 | 1 | 2 |  |  | 5
Assume 100 instructions.
Cycle time = 8ns
Time to execute 100 instructions =1008ns=800ns
Multi-Cycle Processor
Cycle time: =
Execution Time for I instructions:
  =
  Average CPI needed as each instruction takes different number of cycles
Cycle time = 2ns
Given average CPI = 4.6
Time to execute 100 instructions
= 100  4.6  2ns = 920ns


## Slide 31: 5. Comparison of Performance (2/2)
Cycle time:
  = Time for operation in stage k
  N = Number of stages
Execution Time for I instructions:
  =
Single-Cycle Processor
Instruction | Inst Mem | Reg read | ALU | Data Mem | Reg write | Total
ALU (eg: add) | 2 | 1 | 2 |  | 1 | 6
lw | 2 | 1 | 2 | 2 | 1 | 8
sw | 2 | 1 | 2 | 2 |  | 7
beq | 2 | 1 | 2 |  |  | 5
Assume 100 instructions.
Cycle time = 8ns
Time to execute 100 instructions =1008ns=800ns.
Pipelining Processor
Cycle time: =
  = Overhead for pipelining, e.g. pipeline register
Cycles needed for I instructions:
  (need cycles to fill up the pipeline)
Execution Time for I instructions:
  =
Assume pipeline register latency = 0.5ns
Cycle time = 2ns + 0.5ns = 2.5ns
Time to execute 100 instructions
= (100+5–1)  2.5ns = 260ns.


## Slide 32: 5. Pipeline Processor: Ideal Speedup
Assumptions for ideal case:
  Every stage takes the same amount of time 
  No pipeline overhead 
  (Number of instructions is much larger than number of stages)
Conclusion:
Pipeline processor can gain N times speedup, where N is the number of pipeline stages.

## Slide 33: Review Question
Given this code:
  add $t0, $s0, $s1
  sub $t1, $s0, $s1
  sll $t2, $s0, 2
  srl $t3, $s1, 2
How many cycles will it take to execute the code on a single-cycle datapath?
How long will it take to execute the code on a single-cycle datapath, assuming a 100 MHz clock?
How many cycles will it take to execute the code on a 5-stage MIPS pipeline?
How long will it take to execute the code on a 5-stage MIPS pipeline, assuming a 500 MHz clock?

4 cycles
4/(100106) = 40 ns
4 + 4 = 8 cycles
8/(500106) = 16 ns

## Slide 34: End of File