## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Recitation 7
Boolean Algebra, Circuit Design, Simplification

## Slide 2: Agenda
Help Sessions
Townhall
Quick Summary
Solutions to Rec7 Quizzes
Sli.Do Questions
Extra Questions

## Slide 3: summary
Basics of Boolean Algebra

## Slide 4: 2. Boolean Algebra
Truth tables
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | A'
0 | 1
1 | 0
Logic gates
A
B
AB
A
B
A+B
A
A'
Boolean values:
  True (T or 1)
  False (F or 0)
Connectives
  Conjunction (AND)
    A  B; A  B
  Disjunction (OR)
    A + B; A  B
  Negation (NOT)
    A'; ; ;
In CS2100, we use the symbols 1 for true, 0 for false, ∙ for AND, + for OR, and ' for negation (you may use the accent bar). Please follow.

## Slide 5: 2. Boolean Algebra: AND
Do write the AND operator ∙ (instead of omitting it)
  Example: Write a∙b instead of ab
  Why? Writing ab could mean that it is a 2-bit value.

## Slide 6: 4. Precedence of Operators
Precedence from highest to lowest
  Not (')
  And ()
  Or (+)
Examples:
  A  B + C = (A  B) + C
  X + Y' = X + (Y')
  P + Q'  R = P + ((Q')  R)
Use parenthesis to overwrite precedence. Examples:
  A  (B + C) [ Without parenthesis, it means AB+C or (AB)+C ]
  (P + Q)'  R [ Without parenthesis, it means P+Q'R or P+(Q'R) ]
Note the difference with CS1231/CS1231S. Here in CS2100, AND has higher precedence than OR.
Hence, A  B + C is not ambiguous in CS2100.

## Slide 7: summary
Boolean Algebra Laws

## Slide 8: 6. Duality
If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid.
Example:
  The dual equation of a+(bc)=(a+b)(a+c) is a(b+c)=(ab)+(ac).
Duality gives free theorems – “two for the price of one”, as a Boolean equation is logically equivalent to its dual. So, you prove one theorem and the other comes for free!
Examples:
  If (x+y+z)' = x'y'z' is valid, then its dual (xyz)' = x'+y'+z' is also valid.
  If x+1 = 1 is valid, then its dual x0 = 0 is also valid.
Do not confuse duality with negation!

## Slide 9: 5. Laws of Boolean Algebra
Identity laws | 
A + 0 = 0 + A = A | A  1 = 1  A = A
Inverse/complement laws | 
A + A' = A' + A = 1 | A  A' = A'  A = 0
Commutative laws | 
A + B = B + A | A  B = B  A
Associative laws * | 
A + (B + C) = (A + B) + C | A  (B  C) = (A  B)  C
Distributive laws | 
A  (B + C) = (A  B) + (A  C) | A + (B  C) = (A + B)  (A + C)
* Due to the associative laws, A + B + C is unambiguous. It may be evaluated as A + (B + C) or (A + B) + C. Likewise for ABC.

## Slide 10: 7. Theorems
Idempotency | 
X + X = X | X  X = X
One element / Zero element | 
X + 1 = 1 + X = 1 | X  0 = 0  X = 0
Involution | 
( X' )' = X | 
Absorption 1 | 
X + XY = X | X(X + Y) = X
Absorption 2 | 
X + X'Y = X + Y | X(X' + Y) = XY
DeMorgans’ (can be generalised to more than 2 variables) | 
(X + Y)' = X'  Y' | (X  Y)' = X' + Y'
Consensus | 
XY + X'Z + YZ = XY + X'Z | (X+Y)(X'+Z)(Y+Z) = (X+Y)(X'+Z)

## Slide 11: summary
SOP, POS, Minterms, Maxterms

## Slide 12: 10. Standard Forms (2/2)
Sum term
  A single literal or a logical sum (OR) of several literals
  Examples: (1) x, (2) x+y+z', (3) A'+B, (4) A+B, (5) c+d+h'+j
Sum-of-Products (SOP) expression
  A product term or a logical sum (OR) of several product terms
  Examples: (1) x, (2) x + yz', (3) xy' + x'yz, (4) AB + A'B', (5) A + B'C + AC' + CD
Product-of-Sums (POS) expression
  A sum term or a logical product (AND) of several sum terms
  Examples: (1) x, (2) x(y+z'), (3) (x+y')(x'+y+z), (4) (A+B)(A'+B'), (5) (A+B+C)D'(B'+D+E')
Every Boolean expression can be expressed in SOP or POS form.
DLD page 59 Quick Review Questions Questions 3-2 to 3-5.

## Slide 13: 11. Minterms and Maxterms (1/2)
A minterm of n variables is a product term that contains n literals from all the variables.
  Example: On 2 variables x and y, the minterms are:
  x'∙y', x'∙y, x∙y' and x∙y
A maxterm of n variables is a sum term that contains n literals from all the variables.
  Example: On 2 variables x and y, the maxterms are:
  x'+y', x'+y, x+y' and x+y
In general, with n variables we have up to 2n minterms and 2n maxterms.

## Slide 14: 11. Minterms and Maxterms (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3 respectively.
Important fact: Each minterm is the complement of its corresponding maxterm. Likwise, each maxterm is the complement of its corresponding minterm.
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3

## Slide 15: 12.1 Sum-of-Minterms
Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain sum-of-minterms expression by gathering the minterms of the function (where output is 1).
F3 = x'∙y'∙z + x'∙y∙z + x∙y'∙z' + x∙y'∙z = m1 + m3 + m4 + m5 = Sm(1,3,4,5) or Sm(1,3 – 5)
F1 = x∙y∙z' = m6
F2 = x'∙y'∙z + x∙y'∙z' + x∙y'∙z + x∙y∙z' + x∙y∙z = m1 + m4 + m5 + m6 + m7 = Sm(1,4,5,6,7) or Sm(1,4 – 7)


## Slide 16: 12.2 Product-of-Maxterms

Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain product-of-maxterms expression by gathering the maxterms of the function (where output is 0).
F3 = (x+y+z) ∙ (x+y'+z) ∙ (x'+y'+z) ∙ (x'+y'+z') = M0 ∙ M2 ∙ M6 ∙ M7 = PM(0,2,6,7)
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)

## Slide 17: 12.3 Conversion of Standard Forms
We can convert between sum-of-minterms and product-of-maxterms easily
Example: F2 = Sm(1,4,5,6,7) = PM(0,2,3)
Why? See F2' in truth table.
x | y | z | F2 | F2'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
F2' = m0 + m2 + m3 Therefore, F2 = (m0 + m2 + m3)' = m0' ∙ m2' ∙ m3' (by DeMorgan’s) = M0 ∙ M2 ∙ M3 (as mx' = Mx)
  Read up DLD section 3.4, pg 57 – 58.
  Quick Review Questions: pg 60 – 61, Q3-6 to 3-13.

## Slide 18: summary
Basics of Digital Circuits

## Slide 19: 1.1 Inverter/AND/OR Gates
Inverter (NOT gate)
A
A'
A
A'
A | A'
0 | 1
1 | 0
AND gate
A
B
A  B
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR gate
A
B
A+B
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 20: 1.2 NAND/NOR Gates
NAND gate
A | B | (A  B)'
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
(A  B)'
A
B
(A  B)'

NAND
Negative-OR

NOR gate

A
B
(A + B)'
A
B
(A + B)'
A | B | (A + B)'
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR
Negative-AND



## Slide 21: 1.3 XOR/XNOR Gates
XOR gate
A | B | A  B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XNOR gate
A
B
A  B
A
B
(A  B)'
A | B | (A  B)'
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XNOR can be represented by  (Example: A  B)


## Slide 22: Logic Chips
NOT: 74LS04
2-input AND: 74LS08
2-input OR: 74LS32
2-input NAND: 74LS00
2-input NOR: 74LS02

## Slide 23: summary
Analyzing Logic Circuits

## Slide 24: 2.1 Analysing Logic Circuits

Given a logic circuit, we can analyse it to obtain the logic expression.
Example: Given the logic circuit below, what is the Boolean expression of F4?
A'B'
(A'B')+C
((A'B')+C)'
F4 = ((A'B')+C)' = (A+B)C'
F4
A
B
C
DLD page79 Quick Review Questions Questions 4-1 to 4-4.

## Slide 25: summary
Universal Gates

## Slide 26: 3.3 SOP and NAND Circuits (2/2)
Example: F = AB + C'D + E
  Using 2-level NAND circuit
F
A
B
D
C
E
F
A
B
D
C
E
F
A
B
D
C
E

## Slide 27: 3.4 POS and NOR Circuits (2/2)
Example: G = (A+B)  (C'+D)  E
  Using 2-level NOR circuit
G
A
B
D
C
E
G
A
B
D
C
E
G
A
B
D
C
E

## Slide 28: summary
K-Maps

## Slide 29: 5.1 4-Variable K-maps (1/2)
There are 16 square cells in a 4-variable K-map.
Example: Let the variables be w, x, y, z.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 30: Drawing a K-Map from Scratch

## Slide 31: 5.2 How to Use K-maps (1/7)
Based on the Unifying Theorem (complement law):
  A + A' = 1
In a K-map, each cell containing a ‘1’ corresponds to a minterm of a given function F where the output is 1.
Each valid grouping of adjacent cells containing ‘1’ then corresponds to a simpler product term of F.
  A group must have size in powers of two: 1, 2, 4, 8, …
  Grouping 2 adjacent cells eliminates 1 variable from the product term; grouping 4 cells eliminates 2 variables; grouping 8 cells eliminates 3 variables, and so on. In general, grouping 2n cells eliminates n variables.

## Slide 32: 5.2 How to Use K-maps (2/7)
Group as many cells as possible
  The larger the group, the fewer the number of literals in the resulting product term.
Select as few groups as possible to cover all the cells (minterms) of the function
  The fewer the groups, the fewer is the number of product terms in the simplified SOP expression.

## Slide 33: 5.2 How to Use K-maps (3/7)
Example:
F (w,x,y,z) = w'∙x∙y'∙z' + w'∙x∙y'∙z + w∙x'∙y∙z'
+ w∙x'∙y∙z + w∙x∙y∙z' + w∙x∙y∙z
=  m(4, 5, 10, 11, 14, 15)
1
1
1
1
1
1
w
y
00
01
11
10
00 01 11 10
wx
yz
x
z
0
0
0
0
0
0
0
0
0
0

## Slide 34: 5.6 Finding Simplified POS Expression (1/2)
Simplified POS expression can be obtained by grouping the maxterms (i.e. 0s) of the given function.
Example:
  Given F = Sm(0,1,2,3,5,7,8,9,10,11), we first draw the K-map, then group the maxterms together:
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
0
1
1
D
1
1
1
1
1
0
0
0
0
0

## Slide 35: 5.6 Finding Simplified POS Expression (2/2)
This gives the SOP of F' to be F' = BD' + AB
To get POS of F, we have
  F = (BD' + AB)' = (BD')'  (AB)' (DeMorgan) = (B'+D)  (A'+B') (DeMorgan)
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
0
1
1
D
1
1
1
1
1
0
0
0
0
0
K-map of F
0
0
C
A
00
01
11
10
00 01 11 10
B
CD
AB
0
1
0
0
D
0
0
0
0
0
1
1
1
1
1
K-map of F'


## Slide 36: 5.2 How to Use K-maps (7/7)
Examples of valid and invalid groupings.
1
1
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
P
P
1
1
1
1
1
1
1
1
1
1
1
1
1
1
O
1
1
1
1
1
1
O

## Slide 37: summary
Prime Implicants, Essential Prime Implicants

## Slide 38: 5.4 PIs and EPIs (1/3)
To find the simplest (minimal) SOP expression from a K-map, you need to obtain:
  Minimum number of literals per product term; and
  Minimum number of product terms.
Achieved through K-map using
  Bigger groupings of minterms (prime implicants) where possible; and
  No redundant groupings (look for essential prime implicants)
Implicant: a product term that could be used to cover minterms of the function.

## Slide 39: 5.4 PIs and EPIs (2/3)
Prime implicant (PI): a product term obtained by combining the maximum possible number of minterms from adjacent squares in the map. (That is, it is the biggest grouping possible.)
Always look for prime implicants in a K-map.
1
1
1
1
1
1
O
1
1
1
1
1
1
P

## Slide 40: 5.4 PIs and EPIs (3/3)
No redundant groups:
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
O
1
1
Essential prime implicant (EPI): a prime implicant that includes at least one minterm that is not covered by any other prime implicant.
Essential prime implicants

## Slide 41: quizzes

## Slide 42
x’.(y + y’.(z + x.z))’
= x’.(y + y’.z)’ (Absorption 1)
= x’.(y + z)’ (Absorption 2)
!= (x’.(y + z))
NO, they are not equivalent!

## Slide 43
x.((y + y.z) + z)’
= x.(y + z)’ (Absorption 1)
= x.(y’.z’) (De-Morgan’s)
= x.y’.z’ (Associative)
YES, they are equivalent!

## Slide 44
f(a, b, c) = b.c + a.b’
= 1.b.c + a.b’.1 (Identity)
= (a + a’).b.c + a.b’.(c+c’) (Complement)
= a.b.c + a’.b.c + a.b’.c + a.b’.c’ (Distributive)

## Slide 45
g(x, y, z) = (x + y’).(y + z)
= (x + y’ + 0).(0 + y + z) (Identity)
= (x + y’ + z.z’).(x.x’ + y + z) (Complement)
= (x + y’ + z)(x + y’ + z’).(x + y + z).(x’ + y + z)
(Distributive)

## Slide 46
A
B
C
A = x’
B = A.y
= x’.y
C = (B + A)’
= (x’.y + x’)
f = (C + z)
= (x.y + x + z)
= (x + z) (Absorption 1)

## Slide 48
A
B
C
NOT: 1 ns, AND/OR: 2 ns NOR: 3 ns
Timing at A: 0 + 1 = 1 ns
Timing at B = max(y, A) + 2
= max(0, 1) + 2
= 3
Timing at C = max(A, B) + 3
= max(1, 3) + 3
= 6
Timing at f = max(C, z) + 2
= max(6, 0) + 2
= 8 ns

## Slide 53: Sli.do questions

## Slide 54: Slido Questions

## Slide 55: Slido Questions

## Slide 56: Slido Questions

## Slide 57: Slido Questions

## Slide 58: Slido Questions

## Slide 59: Slido Questions

## Slide 60: Slido Questions

## Slide 61: Quick Review Questions #2

DLD page 106, question 5-3.
5-3. Identify the prime implicants and essential prime implicants of the two K-maps below.
0
1
a
b
0
0
1
1
0
1
0
1
00 01 11 10
c
a
bc
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
1
1
1
1
How many PIs?
3 PIs
How many EPIs?
2 EPIs
How many PIs?
7 PIs
How many EPIs?
4 EPIs
0
0
0
0
0

## Slide 62: End of File