## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Recitation-6
MIPS – Processor Control
L12 videos
Prabhu NATARAJAN

## Slide 2: Agenda
MIPS Revision
Quiz questions
Slido Q/A

## Slide 3
Complete Datapath
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX

## Slide 4
1. Identified Control Signals
Control Signal | Execution Stage | Purpose
RegDst | Decode/Operand Fetch | Select the destination register number
RegWrite | Decode/Operand Fetch RegWrite | Enable writing of register
ALUSrc | ALU | Select the 2nd operand for ALU
ALUcontrol | ALU | Select the operation to be performed
MemRead / MemWrite | Memory | Enable reading/writing of data memory
MemToReg | RegWrite | Select the result to be written back to register file
PCSrc | Memory/RegWrite | Select the next PC value

## Slide 5
2. Generating Control Signals: Idea
The control signals are generated based on the instruction to be executed:
  Opcode  Instruction Format
  Example:
    R-Format instruction  RegDst = 1 (use Inst[15:11]) )
  R-Type instruction has additional information:
    The 6-bit "funct" (function code, Inst[5:0]) field
Idea:
  Design a combinational circuit to generate these signals based on Opcode and possibly Function code
    A control unit is needed (a draft design is shown next)

## Slide 6
Inst [25:21]
Inst [20:16]
Inst [15:11]
MUX
Inst [15:0]
MUX
RR1
RR2
WR
WD
RD1
RD2
Register
File
5
5
5
RegWrite
Sign Extend
ALU
result
ALU
ALUcontrol
4
Data
Memory
Address
Read
Data
Write
Data
MemWrite
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
000000
01001
01010
01000
00000
100000
Left Shift 2-bit
PC
Add
4
Add
MUX
PCSrc
Instruction
Memory
is0?
Address
Instruction
RegDst
MemRead
ALUSrc
MemToReg
MUX
Control
The Control Unit (draft)

## Slide 7
3. MIPS Instruction Subset (Review)
016
rs
rt
rd
0
2016
016
2216
016
2416
016
2516
016
2A16
add
sub
and
or
slt
opcode
shamt
funct
R-type
31
25
20
15
10
5
2316
offset
2B16
416
lw
sw
beq
I-type
31
25
20
15
rs
rt
rd
0
rs
rt
rd
0
rs
rt
rd
0
rs
rt
rd
0
rs
rd
offset
rs
rd
offset
rs
rd

## Slide 8
4. Midpoint Check
Control Signal | Execution Stage | Purpose
RegDst | Decode/Operand Fetch | Select the destination register number
RegWrite | Decode/Operand Fetch RegWrite | Enable writing of register
ALUSrc | ALU | Select the 2nd operand for ALU
ALUcontrol | ALU | Select the operation to be performed
MemRead / MemWrite | Memory | Enable reading/writing of data memory
MemToReg | RegWrite | Select the result to be written back to register file
PCSrc | Memory/RegWrite | Select the next PC value
We have gone through almost all of the signals:
  Left with the more challenging ALUcontrol signal
Observation so far:
  The signals discussed so far can be generated by opcode directly
    Function code is not needed up to this point
  A major part of the controller can be built based on opcode alone

## Slide 9: MIPS-Revision
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR

## Slide 10
5. One Bit At A Time (Aha!)
Can you see how the ALUcontrol (4-bit) signal controls the ALU?
  Note: implementation for slt not shown
Acknowledgement: Image taken from NYU Course CSCI-UA.0436
ALUcontrol |  |  | Function
Ainvert | Binvert | Operation | 
0 | 0 | 00 | AND
0 | 0 | 01 | OR
0 | 0 | 10 | add
0 | 1 | 10 | subtract
0 | 1 | 11 | slt
1 | 1 | 00 | NOR

## Slide 11
5. Multilevel Decoding
Now we can start to design for ALUcontrol signal, which depends on:
  Opcode (6-bit) field and Function Code (6-bit) field
Brute Force approach:
  Use Opcode and Function Code directly, i.e. finding expressions with 12 variables
Multilevel Decoding approach:
  Use some of the input to reduce the cases, then generate the full output
  Simplify the design process, reduce the size of the main controller, potentially speedup the circuit

## Slide 12
5. Intermediate Signal: ALUop
Basic Idea:
  Use Opcode to generate a 2-bit ALUop signal
    Represents classification of the instructions:
  Use ALUop signal and Function Code field (for R-type instructions) to generate the 4-bit ALUcontrol signal
Instruction type | ALUop
lw / sw | 00
beq | 01
R-type | 10

## Slide 13
5. Two-level Implementation
opcode
31:26
rs
25:21
rt
20:16
rd
15:11
shamt
10:6
funct
5:0
6
Control
ALU Control
6
ALU
4
ALUcontrol
ALUop
2
00: lw, sw
01: beq
10: add, sub, and, or, slt
0000: and
0001: or
0010: add
0110: sub
0111: set on less than
Step 1.
Generate 2-bit ALUop signal from 6-bit opcode.
Step 2.
Generate ALUcontrol signal from ALUop and optionally 6-bit Funct field.

## Slide 14
5. Generating ALUcontrol Signal

Opcode | ALUop | Instruction Operation | Funct field | ALU action | ALU control
lw |  | load word |  | add | 
sw |  | store word |  | add | 
beq |  | branch equal |  | subtract | 
R-type |  | add |  | add | 
R-type |  | subtract |  | subtract | 
R-type |  | AND |  | AND | 
R-type |  | OR |  | OR | 
R-type |  | set on less than |  | set on less than | 
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
Generation of 2-bit ALUop signal will be discussed later
00
00
01
10
10
10
10
10
xxxxxx
xxxxxx
xxxxxx
10 0000
10 0010
10 0101
10 0100
10 1010
0010
0010
0110
0010
0110
0001
0000
0111
Instruction Type | ALUop
lw / sw | 00
beq | 01
R-type | 10

## Slide 15
5. Design of ALU Control Unit (1/2)

Input: 6-bit Funct field and 2-bit ALUop
Output: 4-bit ALUcontrol
Find the simplified expressions
 | ALUop |  | Funct Field ( F[5:0] == Inst[5:0] ) |  |  |  |  |  | ALU control
 | MSB | LSB | F5 | F4 | F3 | F2 | F1 | F0 | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  | 
or |  |  |  |  |  |  |  |  | 
slt |  |  |  |  |  |  |  |  | 
0
0
X
X
X
X
X
X
0 0 1 0
0
0
X
X
X
X
X
X
0 0 1 0
0
1
X
X
X
X
X
X
0 1 1 0
X
1
0
1
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
1
0
0 1 1 0
1
0
1
0
0
1
0
0
0 0 0 0
1
0
1
0
0
1
0
1
0 0 0 1
1
0
1
0
1
0
1
0
0 1 1 1
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
ALUcontrol3 = 0
ALUcontrol2 = ?
ALUop0 + ALUop1 F1

## Slide 16
5. Design of ALU Control Unit (2/2)
Simple combinational logic
ALUcontrol2
= ALUOp0 + ALUOp1∙F1
ALUcontrol
ALUcontrol3
0
ALUcontrol2
ALUcontrol1
ALUcontrol0
ALU Control block
ALUop
ALUOp0 (LSB)
ALUOp1 (MSB)
F3
F2
F1
F0
F(5-0)
2

## Slide 17
5. Control Design: Outputs

 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
0
0
1
1
0
0
0
1
0
1
1
0
1
0
1
0
0
0
1
X
X
0
1
0
0
0
0
0
X
X
0
0
0
1
0
1

## Slide 18: Final Control Circuit

## Slide 19: Quiz Solutions

## Slide 20: Week-6 MIPS Quiz

## Slide 21: Week-6 MIPS Quiz

## Slide 22: Week-6 MIPS Quiz

## Slide 23: Week-6 MIPS Quiz

## Slide 24: Week-6 MIPS Quiz

## Slide 25: Week-6 MIPS Quiz
1
1
1

## Slide 26: Slido Q/A

## Slide 27: Slido Questions

## Slide 28: Slido Questions

## Slide 29: Slido Questions

## Slide 30: Slido Questions

## Slide 31: Slido Questions

## Slide 32: End of File